Configuration routeurs running config

ROUTEUR-5 :

!
hostname Routeur5
!
memory-size iomem 20
mmi polling-interval 60
no mmi auto-configure
no mmi pvc
mmi snmp-timeout 180
ip subnet-zero
ip cef
!
!
no ip dhcp use vrf connected
!
ip dhcp pool Acces_Autorise
   network 172.16.0.0 255.255.255.0
   dns-server 8.8.8.8
   default-router 172.16.0.1
!
interface FastEthernet0/0
 ip address 172.16.0.1 255.255.255.0
 no shutdown
 duplex auto
 speed auto
!
interface FastEthernet0/1
 no ip address
 shutdown
 duplex auto
 speed auto
!
interface Serial0/1/0
 ip address 13.0.0.1 255.255.255.252
 no fair-queue
 clockrate 56000
!
ip route 0.0.0.0 0.0.0.0 12.0.0.1
!
interface Serial0/1/1
 ip address 12.0.0.2 255.255.255.252

router rip
 network 12.0.0.0
 network 13.0.0.0
 network 172.16.0.0
!
end

ROUTER – 6 :

hostname Routeur6
!
interface FastEthernet0/0
 ip address 10.3.2.2 255.255.254.0
 ip nat outside
 duplex auto
 speed auto
 no shutdown
!
interface Serial0/1/0
 ip address 12.0.0.1 255.255.255.252
 no shutdown
 ip nat inside
 clockrate 56000
!
interface Serial0/1/1
 ip address 14.0.0.2 255.255.255.252
 no shutdown
 ip nat inside
!
router rip
 version 2
 network 10.0.0.0
 network 12.0.0.0
 network 14.0.0.0
 no auto-summary
!
ip route 0.0.0.0 0.0.0.0 10.3.2.1
!
ip nat inside source list PAT interface FastEthernet0/0 overload
!
ip access-list standard PAT
 permit 172.16.0.0 0.0.0.255
 permit 172.31.0.0 0.0.0.255
!
!
line con 0
line aux 0
line vty 0 4
 login
!
end

ROUTEUR-4 :
!
hostname Routeur4
!
boot-start-marker
boot-end-marker
!
!
no aaa new-model
!
resource policy
!
mmi polling-interval 60
no mmi auto-configure
no mmi pvc
mmi snmp-timeout 180
ip subnet-zero
ip cef
!
!
no ip dhcp use vrf connected
!
ip dhcp pool ACCES_REFUSE
   network 172.31.0.0 255.255.255.0
   dns-server 8.8.8.8
   default-router 172.31.0.1
!
interface FastEthernet0/0
 ip address 172.31.0.1 255.255.255.0
 no shutdown
 duplex auto
 speed auto
!
interface FastEthernet0/1
 no ip address
 shutdown
 duplex auto
 speed auto
!
interface Serial0/1/0
 ip address 14.0.0.1 255.255.255.252
 no shutdown
 no fair-queue
 clockrate 56000
!
interface Serial0/1/1
 ip address 13.0.0.2 255.255.255.252
 no shutdown
!
router rip
 network 13.0.0.0
 network 14.0.0.0
 network 172.31.0.0
!
ip classless
!
ip http server
!
control-plane
!
ip route 0.0.0.0 0.0.0.0 14.0.0.2
!
line
con 0
line aux 0
line vty 0 4
 login
!
end